## Slide 1
SOROI BLUE DIANI
Printing Brief
Drinks Menu — Wine List
Artwork Size: 17 × 25 cm | Extent: 11 Sides | Quantity: 25 Sets
Prepared for print production — June 2026

## Slide 2
PRINT
SPECS
Soroi Blue Diani
Wine Menu
SIZE
17 × 25 cm
EXTENT
1 Side Print — 11 Sides Total
SUBSTRATE
250gsm Art Board
PRINTING
Full Colour (CMYK)
FINISHING
Silk Waxed × 2 Sides, Trimmed to Size
QUANTITY
25 Sets
PRICE
KES 14,000/= + VAT

## Slide 3
ARTWORK DIMENSIONS
17 cm
25 cm
ARTWORK
FACE
Dimension Notes
Artwork size:
17 × 25 cm (finished, trimmed)
Bleed:
3 mm on all sides (artwork must extend 3 mm beyond the trim edge)
Safe zone:
5 mm inside the trim edge — keep all critical text and logos within this boundary
Orientation:
Portrait
Colour mode:
CMYK — ensure all files are in CMYK, not RGB
Resolution:
300 DPI minimum at finished size
File format:
Press-ready PDF (PDF/X-1a or PDF/X-4 preferred)

## Slide 4
HOLE PUNCH SPECIFICATION
Binding
Margin
Hole 1
Hole 2
⌀ 5–6 mm
Hole Punch Details
Position:
Left side — binding edge
Number of holes:
2 holes (standard office 2-hole punch pattern)
Hole diameter:
5 mm – 6 mm (standard punch)
Hole spacing:
80 mm centre-to-centre
1st hole centre:
Approx. 85 mm from top edge of finished page
Safe margin:
Minimum 12 mm from left trim edge to text/artwork — keep all content clear of binding margin
Purpose:
For insertion into a ring binder / menu folder
Instruction:
Please drill / punch AFTER trimming to finished size
⚠ Ensure bleed on the left edge accounts for the binding margin. Do not punch through any printed text or logo.

## Slide 5
FILE SUPPLY & PRE-PRESS CHECKLIST
File Supply
Press-ready PDF (PDF/X-1a or PDF/X-4)
CMYK colour mode — no RGB or Pantone unless agreed
300 DPI minimum at finished 17 × 25 cm size
3 mm bleed on all four sides
Crop marks and bleed marks included
All fonts embedded
One file per side — 11 PDF files total
File naming: SoroiBlue_WineMenu_Side[01–11].pdf
Proofing & Sign-off
Digital PDF proof required before press
Hard-copy colour proof required before press
Sign-off by Soroi Collection before printing
No changes permitted after sign-off
Soft-proofing profile: ISO Coated v2 (ECI)
Final files delivered via WeTransfer or Dropbox
Contact for queries (see contact slide)
Delivery to Diani — confirm logistics separately

## Slide 6
SUMMARY & CONTACT
Job Summary
Client
Soroi Blue Diani
Job
Drinks Menu — Wine List
Size
17 × 25 cm
Extent
11 Sides (1 Side Print)
Substrate
250gsm Art Board
Printing
Full Colour CMYK
Finishing
Silk Wax × 2 Sides + Trim
Hole Punch
2 holes, left edge, 80mm spacing, ⌀5–6mm
Quantity
25 Sets
Price
KES 14,000/= + VAT
Contact
The Soroi Collection
reservations@soroi.com
+254 754 351 908
www.soroi.com
For print queries, please quote:
"Soroi Blue Diani — Wine Menu"
and attach this brief.
All artwork and files remain the property of the Soroi Collection. This brief is confidential.